## Slide 1: Planning and Management in Wireless Sensor Networks Qualifying Exam
Adviser：Yeong-Sung Lin
Graduate Student：Cheng-Ta Lee
Department of Information Management
National Taiwan University
Nov. 16 2004

## Slide 2: Outline
I. Introduction to Wireless Sensor Networks
II. Design and Engineering in Wireless Sensor Networks
III. Routing in Wireless Sensor Networks
IV. Research Teams and Related Work
V. Platforms of Wireless Sensor Networks
VI. Future Research Direction and Research Method

## Slide 3: I. Introduction to Wireless Sensor Networks
Hardware Structure and Function for Wireless Sensor Networks
Communication Models
Data Delivery Models
Network Dynamics Models
Wireless Sensor Networks Applications

## Slide 4: Wireless Sensor Networks
Wireless Sensor Networks
  Many (often small) devices
  Wireless communication
  Power by batteries
  Limited processing capabilities
  Often operate in noise and harsh environments
  Monitor and control a physical process or system
“last-meter”

## Slide 5: 鐵路局宜蘭線濁水溪橋自動化安全監控

## Slide 6: Wireless Sensor Networks vs. Ad Hoc Networks [2, 4, 8]
“The number of sensor nodes in a sensor network can be several orders of magnitude higher than the nodes in an ad hoc network”
“Sensor nodes are densely deployed”
“Sensor nodes are prone to failures”
“The topology of a sensor network changes very frequently”
“Sensor nodes mainly use broadcast communication paradigm whereas most ad hoc networks are based on point-to-point communications”
“Sensor nodes are limited in power, computational capacities, and memory”
“Sensor nodes may not have global identification (ID) because of the large amount of overhead and large number of sensors”

## Slide 7: Components of A Sensor Node [8]
Sensing Unit
Processing Unit
Transceiver Unit
Power Unit
Location Finding System
Power Generator
Mobilizer
Power Unit
Power Generator
Location Finding System
Mobilizer
Sensor
ADC
Processor
Storage
Transceiver

## Slide 8: Communication Models [8]

## Slide 9: Sensor Network Model
Event
Sensor Channel
Sensor Node
Sensor Node
Sensor Node
Wireless Channel
Sink

## Slide 10: Data Delivery Models [7]
Sensor networks can be classified in terms of the data delivery required by
  Application (observer)
    Continuous
    Event-driven
    Observer-initiated
    Hybrid
  Routing
    Broadcast
    Unicast
    Multicast

## Slide 11: Network Dynamics Models [7]
Static Sensor Networks
  “In static sensor network, there is no motion among communication sensors, the observer and the phenomenon”
Dynamic Sensor Networks
  “In dynamic sensor networks, either the sensors themselves, the observer, or the phenomenon are mobile”

## Slide 12: Sensor Networks Applications [8]
Military applications
  Monitoring friendly forces, equipment and ammunition
Environmental applications
  Forest fire detection
Health applications
  Telemonitoring of human physiological data
Construction and city management
  Vehicle tracking and detection
Commercial applications
  Environmental control in office buildings
Counterterrorism and public security
  Monitor harmful and dangerous matter

## Slide 13: II. Design and Engineering in Wireless Sensor Networks
Factors Influencing Sensor Network Design
System Evaluation Metrics (QoS)
Individual Node Evaluation Metrics
Communication Architecture in Wireless Sensor Networks
Wireless Sensor Networks Traffic Engineering

## Slide 14: Factors Influencing Sensor Network Design
Fault tolerance [7]
  Lack of power
  Physical damage
  Environmental interference
Scalability [8]
  The number of sensor nodes are huge
    Routing protocol
    Distributive computation
Production costs
  The cost of each sensor node has to be kept low
Hardware constraints [25,26]
  The physical size of each individual sensor node has a significant and direct impact on ease of deployment
Sensor network topology [8]
  Planning and deployment phase
  Post-deployment phase
  Redeployment of additional nodes phase
Environment [8]
  They usually work unattended in remote geographic areas
Transmission media [8]
  Radio
  Infrared
  Optical media
Power consumption [8]
  Sensing
  Communication
  Data processing

## Slide 15: System Evaluation Metrics (QoS) [19]
Lifetime
  The most significant factor in determining lifetime of a given energy supply is radio power consumption
Coverage
  Next to lifetime, coverage is the primary evaluation metric for a wireless network
    Complete coverage
    Complete discriminated
Cost and Ease of Deployment
  A key advantage of wireless sensor networks is their cost and ease of deployment
Response Time
  An alarm must be signaled immediately when an intrusion is detected
Temporal Accuracy
  In environmental and tracking applications, samples from multiple nodes must be cross-correlated in time in order to determine the nature of phenomenon being measured
Security
  Keeping this information secure can be extremely important
Effective Sample Rate
  In a data collection network, effective sample rate is a primary application performance metric

## Slide 16: Individual Node Evaluation Metrics [19]
Power
  To meet the multi-year application requirements individual sensor nodes must be incredibly low-power
  Low duty-cycle
Flexibility
  Node architecture must be flexible
Robustness
  In order to support the lifetime requirements demanded, each node must be constructed to be as robust as possible
Security
  Individual nodes must be capable of performing complex encrypting and authentication algorithms
Communication
  Higher communication rates translate into the ability to achieve higher effective sampling rates and lower network power consumption
Computation
  The two most computationally intensive operations for a wireless sensor node are the in-network data processing and the management of the low-level wireless communication protocols
Time Synchronization
  Errors in the timing mechanism will create inefficiencies that result in increased duty cycles
Size and Cost
  The physical size and cost of each individual sensor node has a significant and direct impact on the ease and cost of deployment

## Slide 17: Communication Architecture in Wireless Sensor Networks [8]
Management plane
  Power management plane
    Manages how a sensor node uses its power
  Mobility management plane
    Detects and registers the movement of sensor nodes
  Task management plane
    Balances and schedules the sensing tasks
Protocol stack
  Physic layer
  Data link layer
  Network layer
  Transport layer
  Application layer

## Slide 18: Physic Layer
The physical layer is responsible for
  Frequency selection
  Carrier frequency generation
  Signal detection
  Modulation
  Data encryption
System on Chip (SoC)
  Micro-Electron-Mechanical-Systems (MEMS)

## Slide 19: Data link Layer
The data link layer is responsible for
  Multiplexing of data streams
  Data frame detection
  Medium access
  Error control
The MAC protocol must two goals
  Creation of the network infrastructure
  Fairly and efficiently share communication resources between sensor nodes

## Slide 20: Media Access Control (MAC) Scheme
Contention-based schemes (CSMA-based) [19]
  Designed for minimum delay and maximum throughput
  Require transceivers to monitor the channel at all times
Reservation-based or schedule-based schemes
  TDMA —a natural choice for sensor networks
Sensor-MAC (SMAC) [15]
  Nodes periodically sleep
  A node sleeps during transmission period of other nodes
  Not suitable for time-critical applications
TDM-FDM Scheme [1]
  Both time and frequency are divided into available transmission slots
  Ton-tx is minimized in TDMA
  Ton-tx is maximized in FDMA

## Slide 21: Network Layer
The networking layer of sensor networks is usually designed according to the following principles:
  Power efficiency is always an important consideration
  Sensor networks are mostly data centric
  Data aggregation is useful only when it does not hinder the collaborative effort of the sensor nodes
  An ideal sensor network has attribute-based addressing
    Data is named by one or more attribute
    Example: [type= humidity, timestamp=01/01/2004/06:30:15, location=60N/90E, humidity=50]

## Slide 22: The power efficiency of the routes [8]
It has the following four possible routes to communicate with the sink
  Route 1: Sink-A-B-T, total PA=4, total α=3
  Route 2: Sink-A-B-C-T, total PA=6, total α= 6
  Route 3: Sink-D-T, total PA=3, total α= 4
  Route 4: Sink-E-F-T, total PA=5, total α= 6
Maximum available power (PA) route: Route 4 is the PA route
Minimum energy (ME) route: Route 1 is the ME route
Minimum hop (MH) route: Route 3 is the MH route
Maximum minimum PA node route: Route 3 is the most efficient and Route 1 is the second efficient paths

## Slide 23: Implosion Problem and Overlap Problem
The implosion problem The overlap problem

## Slide 24: Data Aggregation [9]
“The data aggregation is a technique used to solve the implosion and overlap problems in data-centric routing”

## Slide 25: Grouping [3]
A sensor network (left) with an in-network, grouped aggregate applied to it (right)

## Slide 26: Addressing for Wireless Sensor Networks
An address-free architecture
  Not applicable when static addressing of nodes is needed
  Identifier conflict
Special addressing requirement
  Local unique addresses
    Example: What is the humidity at sensor #192.168.84.2 ?
  IPv6

## Slide 27: Transport Layer and Application Layer
“Transport layer is especially needed when the system is planned to be accessed through Internet or other external” networks
Protocol
  TCP
  UDP
Three possible application layer protocols
  Sensor Management Protocol (SMP)
    “SMP needs to access the nodes by using attribute-based naming and location-based addressing”
  Task Assignment and Data Advertisement Protocol (TADAP)
    “Users send their interest to a sensor node, a subset of the nodes or whole network”
  Sensor Query and Data Dissemination Protocol (SQDDP)
    “SQDDP provides user applications with interfaces to issue queries, respond to queries and collect incoming replies”

## Slide 28: Wireless Sensor Networks Traffic Engineering [36]
Traffic Analysis and Modeling
Network Planning
  Minimum installation and operation cost subject to performance (QoS)
Network Performance Optimization
  For an in-service traffic network, to assure pre-specified QoS requirements and/or to optimize certain performance measures
Network Performance Monitoring
  To collect traffic measurements for load forecasting purposes (to feed the servicing and the capacity expansion processes)
Network Servicing
  Traffic rerouting
  Resource reallocation
  capacity augmentation (minimal-cost capacity augmentation to satisfy the current demand)
Network Capacity Expansion
  The total cost, considering the effect of economies of scale and composite cost of money, is minimized
Network
Planning
Performance
Assurance &
Optimization
Network
Monitoring
Network
Servicing
Network
Capacity
Expansion
Traffic
Analysis

## Slide 29: III. Routing in Wireless Sensor Networks
Flat Routing Protocols
  Direct Communication
  Multi-hop Routing Protocols
  SPIN [9]
  Directed Diffusion [10]
Hierarchical Routing Protocols
  LEACH [11]
  TEEN [20]

## Slide 30: Direct Communication
Sink
Sensor node
Sensor nodes communicate with the sink directly
Energy consumption: Rn, 2≦n≦6

## Slide 31: Multi-hop Routing Protocols
Sink
Transmit through some other intermediate nodes
Implosion and overlap problems
Sensor node

## Slide 32: SPIN (1/2)
Sensor Protocols for Information via Negotiation.
ADV and REQ are metadata message.

## Slide 33: SPIN (2/2)
Key results of the unlimited energy simulations for the SPIN-1, flooding, and gossiping protocols compared with the ideal data distribution protocol.
Performance | Protocol |  | 
 | SPIN-1 | Flooding | Gossiping
Energy Dissipation | 0.4J | 6.3J | 44.1J
Convergence Time | 90 ms | 10 ms | 3025 ms

## Slide 34: Directed Diffusion
Simplified schematic for directed diffusion
  (a) Interest (query) propagation
  (b) Initial gradients (data matching the interest) setup
  (c) Data (event) delivery along reinforced path

## Slide 35: Hierarchical Routing Protocols
Clustering A cluster hierarchy

## Slide 36: Clustering Sensor Network Architecture

## Slide 37: LEACH (1/3)
Low-Energy Adaptive Clustering Hierarchy
  Randomly rotating the cluster-head among sensors
  Low energy consumption
  Low Diameter
Cluster head
Sink
Cluster

## Slide 38: LEACH (2/3)
“During the set-up phase, a sensor node chooses a random number between 0 and 1. If this random number is less than the threshold T(n), the sensor node is a cluster-head. T(n) is calculated as”

## Slide 39: LEACH (3/3)
Dynamic cluster formation during two different rounds of LEACH
Lifetime: 15%↑
Proactive
  Suitable for periodicity applications

## Slide 40: TEEN
Threshold sensitive Energy Efficient sensor Network protocol
Threshold
  Hard Threshold (HT ): “This is a threshold value for the sensed attribute. It is the absolute value of the attribute beyond which, the node sensing this value must switch on its transmitter and report to its cluster head”
  Soft Threshold (ST ): “This is a small change in the value of the sensed attribute which triggers the node to switch on its transmitter and transmit”
Reactive
  Suitable for time-critical applications

## Slide 41: IV. Research Teams
Overseas Research Organizations
  MIT [3,12]
    μAMPS(μ-Adaptive Multi-Domain Power Aware Sensors)
    LEACH(Low Energy Adaptive Clustering Hierarchy)
    SPIN (Sensor Protocols for Information via Negotiation)
  UCLA [13, 29]
    WINS (Wireless Integrated Network Sensors)
      “Provide distributed network and Internet access to sensors, controls, and processors”
  U.C. Berkeley [25, 28]
    Smart dust
    PicoRadio
      Develop a ‘‘system-on-chip (SoC)’’ implementation of a PicoNode
    NEST (Network Embedded System Technology)
      TinyOS
Project Plans of National Science Council [37]
  無線感測網路之關鍵技術及在社區照護之應用─子計畫四 (93年度)
    王勝德
    國立臺灣大學電機工程學系暨研究所
    執行起迄：20040801～20050731
    核定金額： 624,800 元
  …
Network Optimization Research Laboratory
  Frank Y.S. Lin and P.L. Chiu , “A Near-optimal Sensor Placement Algorithm to Achieve Complete Coverage/Discrimination in Sensor Networks,” IEEE Communications Letters, January, 2005
  Chih-Wei Shiou, Advisor：Dr. Frank Yeong-Sung Lin, “Optimal Energy-Efficient Routing for Wireless Sensor Networks,” NTU, July, 2004
  Keng-Hung Yeh, Advisor：Dr. Frank Yeong-Sung Lin, “An Energy-Efficient Routing Algorithm for The Maximization of System Lifetime in Wireless Sensor Networks,” NTU, July, 2004

## Slide 42: Related Work (1/4)
Physical Layer [1, 4]
Simple and low-power modulation schemes
Hardware design
Table 4.2 Useful sleep states for the sensor node
State | SA-1110 | Sensor, A/D | Radio
Active(s0) | active | sense | tx/rx
Ready(s1) | idle | sense | rx
Monitor(s2) | sleep | sense | rx
Observe(s3) | sleep | sense | off
Deep Sleep(s4) | sleep | off | off
Table 4.3 Sleep state power and latency
State | Pk(mW) | τk(ms)
Active | 1040 | -
Ready | 400 | 5
Monitor | 270 | 15
Look | 200 | 20
Deep Sleep | 10 | 50

## Slide 43: Related Work (2/4)
Data Link Layer [4]
Self-organization
Power saving modes of operation
Table 4.4 A qualitative overview of MAC protocols for sensor networks
MAC protocol | Channel access mode | Sensor network specifics | Power conservation
SMACS[14] | Fixed allocation of duplex time slots at fixed frequency | Exploitation of large available bandwidth compared to sensor data rate | Random wake up during setup and turning radio off while idle
Hybrid TDMA/FDMA[1] | Frequency and time division | Optimum number of channels calculated for minimum system energy | Hardware-based approach for system energy minimization
CSMA-based | Contention-based random access | Designed for minimum delay and maximum throughput | Constant listening time for energy efficiency
Sensor-MAC (SMAC)[15] | Nodes periodically sleep and wake up. Not suitable for time-critical applications | A node sleeps during transmission period of other nodes. | Nodes periodically sleep and turning radio off while sleep

## Slide 44: Related Work (3/4)
Network Layer [4, 6]
Table 4.5 An overview of network layer schemes
Network layer scheme | Description
Flooding | Broadcasts data to all neighbor nodes regardless if they receive it before or not
Gossiping | Sends data to one randomly selected neighbor
SPIN[9] | Sends data to sensor nodes only if they are interested; has three types of messages (i.e., ADV, REQ, and DATA)
Directed diffusion[10] | Sets up gradients for data to flow from source to sink during interest dissemination
LEACH[11] | Forms clusters to minimize energy dissipation, LEACH protocol for proactive networks
TEEN[20] | Threshold sensitive Energy Efficient sensor Network protocol for reactive networks

## Slide 45: Related Work (4/4)
Application Layer [6]
  Security
  Object tracking
Fig. 4.4 (a) A detects the incoming vehicle
(b) the sensing activities of C, D, and E are suppressed but B starts tracking again
(c) the vehicle comes into B's area and C restarts its sensor
(d) C and D detect the vehicle and E's sensor is restarted
(e) the vehicle goes out of A and B's ranges
(f) sensing activity at A stops

## Slide 46: V. Platform of Wireless Sensor Networks
IEEE 802.15.4 [30, 32]
  Maximum economic efficiency
    Standardization
  Low-Rate Wireless Personal Area Network (LR-WPAN)
    Physical Layer
    Data Link Layer
  Characteristics of 802.15.4
    2.4GHz, 915MHz, 868Mhz
    Star, Peer to Peer, Cluster Tree
    IEEE 802.11 CSMA/CA
    64 bits (Extended Address) and 16 bits (Short Address)
    Low energy consumption
TinyOS [28]
  It is based on an event driven execution engine that simultaneously provides efficiency and fine-grained concurrency
  TinyOS 1.1.7 (2004/7)
Hardware Platform

## Slide 47: Hardware Platform
http://www-unix.mcs.anl.gov/~beckman/wireless-sensor-networks/Intro-Sensor-Nets.pdf

## Slide 48: VI. Future Research Direction
Structural design of Wireless Sensor Networks
Media access control schemes
Sleeping schedule
Fault tolerance
Energy and resource management
Sensor deployment
Object monitoring and tracking

## Slide 49: Research Method [23]
“As a decision-making tool, mathematical programming is both a science and an art”
The principal phases for implementing mathematical programming in practice include:
  Definition of the problem
  Construction of the model
  Solution of the model
  Validation of the model
  Implementation of the solution

## Slide 50
Thank You!
Q & A

## Slide 51: References (1/4)
E. Shih, S. Cho, N. Ickes, R. Min, A. Sinha, A. Wang, A. Chandrakasan, “Physical layer driven protocol and algorithm design for energy-efficient wireless sensor networks,” Proceedings of ACM MobiCom’01, Rome, Italy, pp. 272-286, July 2001.
C. E. Perkins, “Ad Hoc Networks,”Addison-Wesley, 2001
Anna Hac, “Wireless sensor network designs,” Wiley, 2003.
I.F. Akyildiz, W. Su, Y. Sankarasubramaniam, E. Cayirci, “A Survey on Wireless sensor network,”IEEE Communication Magazine, pp. 102-114, August 2002.
Frank Y.S. Lin and P.L. Chiu , “A Near-optimal Sensor Placement Algorithm to Achieve Complete Coverage/Discrimination in Sensor Networks ,” IEEE Communications Letters, (to appear).
C.C. Shen, C. Drisathapornphat, and C. Jaikaeo,“Sensor Information Networking Architecture and Applications,” IEEE Personal Communications, Augest 2001.
S. Tilak, B. Abu-Ghazaleh, and W. Heinzelman, “A Taxonomy of wireless micro-sensor network models,” Mobile Computing and Communications Review, vol. 1 no. 2, 2002.
I.F. Akyildiz, W. Su, Y. Sankarasubramaniam, E. Cayirci, “Wireless sensor network: a survey,”Computer Networks , vol. 38, pp. 393-422, 2002.
W. Heinzelman, J. Kulik, and H. Balakrishnan, “Adaptive Protocols for Information Dissemination in Wireless Sensor Networks,” in Proceedings of the Fifth Annual ACM/IEEE International Conference on Mobile Computing and Networking (MobiCom ’99), pp. 174-185, Aug. 1999.
C. Intanagonwiwat, R. Govindan, D. Estrin, J. Heidemann, F. Silva, “Directed diffusion for wireless sensor networking,” IEEE/ACM Transactions on Networking, vol. 11, no. 1, pp. 2-16, Feb. 2003.

## Slide 52: References (2/4)
W. B. Heinzelman, P. Chandrakasan, and H. Balakrishnan, “An application-specific protocol architecture for wireless microsensor networks,” IEEE Transactions on Wireless Communications, vol. 1, no. 4, pp. 660-670, Oct. 2002.
MIT,” μ-Adaptive Multi-domain Power aware Sensors,” http://www-mtl.mit.edu/research/icsystems/uamps, 2004.
UCLA,” Wireless Integrated Network Sensors,” http://www.janet.ucla.edu/WINS, 2004.
K. Sohrabi, J. Gao, V. Ailawadhi, G.J. Pottie, “Protocols for self-organization of a wireless sensor network,” IEEE Personal Communications, pp. 16-27, Oct. 2000.
W. Ye, J. Heidemann, D. Estrin, “An energy-efficient MAC protocol for wireless sensor networks,” IEEE INFOCOM 2002, pp. 1567-1576, 2002.
Chih-Wei Shiou, Advisor：Dr. Frank Yeong-Sung Lin, “Optimal Energy-Efficient Routing for Wireless Sensor Networks,” NTU, July, 2004.
Keng-Hung Yeh, Advisor：Dr. Frank Yeong-Sung Lin, “An Energy-Efficient Routing Algorithm for The Maximization of System Lifetime in Wireless Sensor Networks,” NTU, July, 2004.
Chi-Fu Huang, Yu-Chee Tseng, “The Coverage Problem in a Wireless Sensor Network,” WSNA, Sep. 19, 2003.
Jason Lester Hill, “System Architecture for Wireless Sensor Networks,” Chapter 1 and 2, UC, Berkeley, 2003.
A. Manjeshwar and D.P. Agrawal. “TEEN: a Routing Protocol for enhanced efficiency In wireless sensor networks,” Parallel and Distributed Processing Symposium., Proceedings 15th, pp. 23-27 April 2001.

## Slide 53: References (3/4)
Budhaditya Deb, Sudeep Bhatnagar and Badri Nath, “A Topology Discovery Algorithm for Sensor Networks with Applications to Network Management,” in IEEE CAS workshop, September 2002.
A. bharathidasan, V.A.S. Ponduru, “Sensor Networks: an Overview,” Potentials, IEEE, pp20-23, April-May 2003.
Hamdy A. Taha, “Operations Research: an Introduction,” chapter 1, seventh edition, 1982.
“ALERT” http://www.alertsystems.org.
U.C. Berkeley,” Smart Dust Project,” http://robotics.eecs.berkeley.edu/~pister/SmartDust,2004.
U.C. Berkeley,”A smart dust mote,” http://www.coe.berkeley.edu/labnotes/0701brainybuildings.html.
U.C. Berkeley,” NEST Project,” http://webs.cs.berkeley.edu/nest-index.html.
TinyOS Community Forum, “TinyOS,” http://www.tinyos.net.
G.J. Pottie, W.J. Kaiser, “Wireless integrated network sensors”, Communications of the ACM 43 (5), pp.551–558. 2000.
IEEE,” IEEE 802.15 Working Group for WPAN,” http://ieee802.org/15/index.html, 2004.

## Slide 54: References (4/4)
Sensor Hardware, http://www.ece.cmu.edu/~adrian/projects/mc2001/node2.html.
吳健豪, 尹華強, 許獻聰,” 感測網路的技術與進展,” 通訊雜誌, 116, pp.64-69, Sep. 2003
韓永祥, 王藏億,” Survey of Wireless Sensor Networks,” http://www.cm.nctu.edu.tw/Chinese/seni/dm/nm5.htm, 2004.
莊裕澤博士, “Distributed Systems, Synchronizing Physical Time, and Mobile Computing,” 分散式系統上課講義, 2002.
孫雅麗博士, “IEEE 802.11b – Wireless LAN,” 高等計算機網路上課講義, 2002.
林永松博士, “Network Planning and Capacity Management,” 高等計算機網路上課講義, 2003.
國科會, “92至93年度無線感測器網路相關專題研究計畫” http://web.nsc.gov.tw, 2004.