## Slide 1: 論文進度報告
Advisor: Prof. Frank Yeong-Sung Lin presented by Yi-Wei Li

## Slide 2: Agenda
Introduction
Notation and Problem Formulation
LR problem and subproblems
Heuristics

## Slide 3: Title
Joint flow control, capacity allocation and routing to achieve end-to-end delay and throughput fairness in wireless mesh networks
基於配置頻寬、流量控制與路由決策達成具端點至端點延遲及吞吐量公平之無線網狀網路營運

## Slide 4: Introduction

## Slide 5: Introduction

## Slide 6: Problem description
Given :
  Network topology
  The capacity of mesh routers and gateways
  The traffic rate required by each mesh client
Objective :
  To maximize the minimum rate of all clients

## Slide 7: Problem description
Subject to :
  Routing constraints
  Mobile host constraints
  Link capacity constraints
  QoS constraints
  Link constraints
  Flow control constraints
To determine :
  The end-to-end delay
  The data rate of clients

## Slide 8: Notation and Problem Formulation

## Slide 9
Introduction of Notations | 
N | The set of mesh clients, where nN.
R | The set of mesh routers, where rR.
G | The set of gateways, where gG.
 | The nodal capacity of router r.
 | The air-interface capacity of router r.
 | The capacity of wired line on gateway g.
 | The average delay on link ij, which is a function of aggregate flow fij and capacity cij.

## Slide 10
Introduction of Notations | 
 | The average delay on host n to router r, which is a function of transmission rate and air-interface capacity .
Prg | A given set of simple directed paths from the router r to the gateway g , where p Prg
 | The indication function which is 1 if link from router i to router j is on path p and 0 otherwise.
 | (pkt/sec) The arrival rate of each client nN.
ij | A given link utilization factor which keeps link ij from saturated.
Rr | The service range of mesh router r.

## Slide 11
Introduction of Notations | 
knr | 1 if mobile client n associates to mesh router r and 0 otherwise.
n | A given delay priority factor which equals to 1 means delay of client nN equals to D and n is inverse proportional to the priority of client n. The lower value of n means client n enjoy less end-to-end delay.

## Slide 12
Introduction of decision variables | 
γn | (pkt/sec) The allowed arrival rate of new traffic for each client nN.
yn | (pkt/sec) The rejected arrival rate of new traffic for each client nN.
 | (pkt/sec) The link capacity (air-interface) of router r to client n.
fij | (pkt/sec) The aggregated flow of each link ij.
cij | (pkt/sec) The allocated capacity (nodal) of each link ij.
xp | A routing decision variable which is 1 when path pPrg is used to transmit the packets for client n and 0 otherwise.

## Slide 13
Introduction of decision variables | 
trij | 1 if link ij is on the path adopted by mesh router r and 0 otherwise.
zrg | 1 if router r connects to the wired network via gateway g and 0 otherwise.
D | The end-to-end delay requirement.

## Slide 14: Problem formulation

## Slide 17: LR problem and subproblems

## Slide 18
We relax constraints 1, 4, 7, 9, 11, 12, 14, 15, 16, 18, 20, 5 to (LR) with LR multipliers
. .
are unrestricted and are non-positive.

## Slide 22
Compute the coefficient of S for each client n
Choose the minimum one and If
  Positive  assign 0 to S
  Negative  assign to S

## Slide 24: Sub 2
If knr = 0
  Set all to 0.
  Calculate the coefficient of , and choose the minimum one. Set , .
  Repeat step 2 until .
Else
  Let , where E is a discrete capacity set.
  the obj =
  For each , we analysis the objective function and find the minimum value.

## Slide 26: Sub 3
Set all ar to 0.
Calculate coefficient of ar with zrg =0 and zrg =1.
Choose the smallest one and set the value zrg and
Repeat step 3 until is satisfied.

## Slide 28: Sub 4
Let .
For each r with cij , solve .
Sort these fij .
At each interval, analysis the local minimum value.
The global minimum point can be found by comparing these local minimum points.

## Slide 29: Getting Primal Feasible Solutions

## Slide 30: Getting Primal Feasible Solutions
Step1: Run gateway_selection_heuristic
Step2: Run routing_heuristic
Step3: Run flow_control_heuristic
Step4: Run capacity_adjust_heuristic
Step5: examine the latency we can tolerance or not
Y: End
N: go back to Step1.

## Slide 31: Gateway_selection_heuristic
Step 1: Initial gateway selection assignment according to zrg.
Step 2: Find the gateway g that violate capacity most seriously. If not found, the stop.
Step 3: For each router r belonging to gateway g, we sort by ar and choose the smallest one.
Step 4: For this r with ar, we reassign to another gateway with smallest hop-count distance.
Step 5: Repeat step 2, 3, and 4 until all clients can be admit.

## Slide 32: Routing_heuristic
Step 1: set the arc weight for each link to be the coefficient of variable xp.
Step 2: run Dijkstra’s algorithm to get the shortest path from each router.

## Slide 33: Flow_control_heuristic
With given path, we implement max-min flow control to calculate how much rate a client can transmit.
Input rate vector of all flows start at zero;
Equivalent increase the rates on all paths together until the bit rates of some flows are constrained by the capacity set;
Freeze the bit rate of these flows;
Apply step 2 repeatedly to non-frozen flows until the bit rate of all flows are constrained by the capacity set.

## Slide 34: Capacity_adjust_heuristic
Step 1: For each leaf router r, examine the latency violating QoS constraint or not. If not, compute the aggregated flow and transmit to it’s next router.
Step 2: In this router r, select cir with the smallest coefficient (or ∆D) and cjr with the largest coefficient (or ∆D), reallocate the capacity in such a way .
Step 3: Repeat Step 2 until all Dr’r are the same.
Step 4: Go to Step 1 until we calculate the gateway capacity allocation.

## Slide 35: Thanks for Your Listening!